## Slide 1: Introduction to C
Class 23

## Slide 2: Agenda
Preparation and Concepts
C basics
Program structure
Data types
Operators
Summary
Notes: Instructor:
The main objective of this class was to introduce students to C programming. After this lecture students should have a good understanding of the following:
C basics – including primary differences between MATLAB and C
The general structure students will use to write C programs
The declaration of variables and the common data types associated with variables students will use
Operators – including assignment, increment/decrement, relational, and logical. Students should recognize the similarities and differences between the operators in C and in MATLAB

## Slide 3: Preparation
Assignment:
  Read C: How to Program
  Watch the video: PRE_23_C_Intro_VIDEO
Understand the following:
  Preprocessor directives
  Declaration of variables
  Comments in C
  How the main()functions works
Notes: Instructor:
This slide is to serve as a reminder regarding the specific assignments students completed as preparation for today’s class.
Assignment:
Read C: How to Program pgs. 41-52, 93-96
Watch the video: PRE_23_C_Intro_VIDEO

## Slide 4: Preparation
Understand the following:
  Assignment operators
  Increment and decrement operators
  How the ; symbol is used in C
  How math operations work in C

## Slide 5: Concept Comprehension
Chart: PRE 23-1 Understand the Best
| preprocessor directives | declaration of variables | comments in C | How the main() function works | assignment operators | increment operators | How the ; symbol is used in C | How math operations work in C
 | 35 | 41 | 185 | 25 | 20 | 14 | 13 | 11
 | 203 | 140 | 87
Chart: PRE 23-1 Questions
| preprocessor directives | declaration of variables | comments in C | How the main() function works | assignment operators | increment operators | How the ; symbol is used in C | How math operations work in C
 | 102 | 18 | 8 | 75 | 9 | 48 | 63 | 21
 | 203 | 140 | 87
Notes: Instructor:
Concept Comprehension pie charts come from PRE B23-1 2014. Results have been consistent year to year.
This is an opportunity to ask students about the things they understand the best and the least from the preparation material.
Students feel they understand comments in C the best. This is a good time to verify this and ask students about comments in C.
You may also want to spend some time asking the class about preprocessor directives and explain them in more detail. Another topic that students have questions on is how the main() function works. This is a good opportunity to make a comparison to MATLAB script files.

## Slide 6: C Program Basics
C vs. MATLAB
    Compiled compared to interpreted
    Variable declaration
    Preprocessor directives – #include, #define
Notes: Instructor:
At this point, students are familiar with MATLAB. We can introduce students to C Program Basics through comparisons with MATLAB.
For both languages, you will use an editor to write your program. In the editor, you write instructions that look like everyday language and contains commonly used mathematical notations. You can read and understand what you write. MATLAB is an interpreted language. The program gets compiled when you run it, so MATLAB must interpret each line of code you wrote for your program and convert it to something the computer will understand. In C, you must compile the program you wrote in the editor. The compiler acts as a translator to covert the high-level language of your program into machine language. The result is an executable file you can run that the computer will already understand. Since MATLAB interprets the high-level language only when you run the program, the program will run slower than a compiled program.
Another difference is that in C, we must declare variables before we can ever use them. We have to set aside space in memory for the variable before we can assign anything to the variable. This is not something we had to do in MATLAB.
Additionally, we must include preprocessor directives in C, which is not something we had to do in MATLAB. We will cover this in more detail in a few slides, but this is a good time to introduce the topic and ask students to describe what preprocessor directives do or to provide examples of what they are.
(D&D – Sections 1.4 – 1.7, Sections 2.1 – 2.4, Sections 13.1 – 13.4)

## Slide 7: Keywords
MATLAB
C
sizeof
while
otherwise
else
for
elseif
break
char
default
enum
int
goto
Notes: Instructor:
Certain words have a special meaning to the C compiler. They are called reserved words or keywords. We should not try to use these words as names of variables or function names in a program. This is similar to MATLAB. MATLAB also has reserved words such as else, while, etc. Also, recall that MATLAB had a number of built-in functions and you did not want to use the built in function names as the names of variables or functions you created.
Note that while there may be overlap between the words in MATLAB and C, the way they are used and their function may differ. Bold words on the slide exist ONLY in the language specified.
This slide shows just a small sample of keywords.
The keyword list for C contains 32 words (D&D – Section 2.6).

## Slide 8: Standard Program Structure
/* Comment statements */
/* Include header files */
#include <stdio.h>
/* MY_CONSTANT is a gain factor
#define MY_CONSTANT 10
int main()
{
/* Declare/initialize variables */
int a = 30, b;
/* Multiply by gain factor */
b = MY_CONSTANT*a;
}
Comment statements
Pre-processor directives
Declaration statements
One or more functions
      main() function
Executable statements
Notes: Some things to consider pointing out here:
There should be comments at the start of your program that explains what’s going on and who wrote it and when, that is, some documentation so whomever is looking at it can get a sense of the context right at the start.
We will need to use #include to include the library files that we need to make some of the built in functions work. Different functions require different libraries. So, depending on what we’re doing the #include list could be long or it could be short.
We probably won’t truly need any defined constants, but we should make use of them. Partly by defining these constants with words or phrases that have meaning to us, it will make programs easier to understand. Also, if we decide to change the value of a constant, we can change it in one place, and it will update throughout the program. Don’t forget, these are constants. Their value cannot be changed and a defined constant can never be assigned a value within the body of a program (i.e., you’ll never see a defined constant on the LHS of the =.
C requires that we set up a data type for each variable so that it knows how much memory space to dedicate to that variable, which in turn dictates how big of a value can be stored in the variable. This step is called declaring the variable. It is common that all variables are declared at the beginning of the function and then used throughout the rest of the function. However, it is possible to declare variables immediately before using them.
Depending on how much time you want to spend on this, you might take the opportunity to ask what the difference is between the declaration of ‘a’ as an integer and the declaration of ‘b’ as an integer.
The last part of the main() function is the executable part, where the variables and functions and constants are used.

## Slide 9: Standard Program Structure
/* Comment statements */
/* Include header files */
#include <stdio.h>
/* MY_CONSTANT is a gain factor
#define MY_CONSTANT 10
int main()
{
/* Declare/initialize variables */
int a = 30, b;
/* Multiply by gain factor */
b = MY_CONSTANT*a;
}
Comment statements
Pre-processor directives
Comment statements
Declaration statements
Comment statements
One or more functions
Comment statements
Executable statements
Comment statements
Notes: The main point of this is to remind students that comments are to be used liberally throughout their code for two reasons. One, they should put the comments in first as a way of designing and planning the code they plan to write. If they can explain what the code is supposed to do, then they can write the actual C language commands to make it happen. Until they have that understanding, it will be more difficult to figure out what part of the language to use.
Two, comments make it so someone else can understand their code. That may not be a big deal for the programs written in this class, but it’s a good habit to be in for when they write larger, more complex programs.

## Slide 10: Comment Statements
…
/* Formal comments are typically long and often span several lines */
…
//Informal comments last only
//to the end of the line
…
d = 10.5; //diameter (meters)
…
Formal comments
      /* Comments */
Informal comments
      only in C++, not C
      // Comments
Notes: Instructor:
Formal Comments:
  Used for detailed description of functions or operations (for our benefit, not compiler’s).
  Can take multiple lines in source file.
It is important to highlight that “informal” comments exist only in C++. We are currently working in programming in C, but the computer has a C++ compiler, which means the computer will recognize and understand the use of “informal” comments if you use them now.

## Slide 11: Pre-Processor Directives
…
#include <stdio.h>
…
#define E 2.7182818
#define PI 3.14159265359
…
…
Header files for library functions
#include <library>
Define constants and macros
#define name value
Note Space
Note Spaces
Notes: Instructor:
The preprocessor in C instructs the compiler to do required pre-processing before the actual compilation. Examples of preprocessor directives in C that we will use are #include and #define. #include allows us to include header files in our program, which provides us access to various libraries. This is an opportunity to again make the comparison to MATLAB. In C, if I want to use a certain function then I have to include the header file for that library. This is not something we had to do in MATLAB.
#define allows us to create constants to be used throughout our program. It defines a symbolic constant. A symbolic constant is an identifier that’s replaced with replacement text by the C preprocessor before the program is compiled. When the program is preprocessed, all occurrences of the symbolic constant are replaced with the replacement text. For example, everywhere in the program where you would see PI would be replaced with 3.14159265359.
(D&D – Section 6.4).

## Slide 12: Declarations
//Preprocessor directives
…
int main()
{
int a, b, c;
float r, p, q;
double x, y, z;
char m, n, o;
…
…
}
Variable names
Data types
Notes: Instructor:
All variables must be defined with a name and a data type before they can be used in a program. In C, when you define a variable, you set aside a location in memory where values can be stored and later used by the program.
There are two types of variables in C: fundamental and derived. In a few weeks we will discuss derived data types, but for now we will start by looking at the four fundamental data types: int, float, char, and double.

## Slide 13: Data Types
Integer variables
Floating point variables
…
int a = 10, b = 5.9;
float q = 5, r = 10.2;
fprintf(stdout,"%i\n%i\n%f\n%.2f\n",a,b,q,r);
…
Notes: Instructor:
While there are multiple data types, int and float are very common and we will use them often.
WHITEBOARD ACTIVITY – Have students determine the output.
The next slide contains the answer.

## Slide 14: Data Types
Integer variables
Floating point variables
…
int a = 10, b = 5.9;
float q = 5, r = 10.2;
fprintf(stdout,"%i\n%i\n%f\n%.2f\n",a,b,q,r);
…
10
5
5.000000
10.20
Notes: Instructor:
Spend some time pointing out what happens to the value stored in “b” since it was declared as an integer. This will become even more important when we get to C arithmetic. Point out what happens to the value stored in “q” since it was declared as a float. You can also point out the difference in formatting between q and r as a way to remind students of how the formatting for fprintf works. It works the same in C as it did in MATLAB.

## Slide 15: Internal Storage
  Binary digit (bit) -- 0 or 1
  Byte – usually 8 bits
  Word -- often 4 bytes
0
1
0
0
1
1
1
1
1
1
0
0
0
1
1
0
1
0
0
0
1
1
1
1
1
0
0
0
0
1
1
0
0
0
1
1
1
1
0
0
0
= 93
= 1,562,840,268
0
Notes: Instructor:
Decimal values are included to show how a decimal value converts to binary.
First column to the right is 2^0, next is 2^1, 2^2, etc.

## Slide 16: Internal Storage
Note on binary - when reading a larger binary number, each 'place' of the number represents a power of 2, starting from 0 and usually reading right to left
1
1
0
1
4

## Slide 17: Internal Storage
System-specific
    int – 4 bytes
    float – 4 bytes
    double – 8 bytes
    char – 1 byte
Notes: Instructor:
This is a chance to tie the material together. Students first learned they must declare variables to allocate space in memory, then they learned about various data types, now you can show how much storage is reserved for those specific data types.
Make sure to note, these are common sizes for data types. It does depend on the machine, but this is what the internal storage looks like for us.

## Slide 18: Arithmetic
Addition (+)
Subtraction (-)
Multiplication (*)
Division (/)
Remainder (%)
Exponent (pow(a,b))
      Requires math.h library
Standard order of operations
#include <math.h>
...
int x=5, y=2;
float a=5,b=2.5,c=2,d,e,f,g;
d = (a+b)*(b-c);
e = pow(c,2);
f = d/e;
g = x%y;
…
d = 3.750000
e = 4.000000
f = 0.937500
g = 1.000000
Notes: Instructor:
This is yet another chance to make a comparison to MATLAB.
QUESTION – what operation did we have in MATLAB that we don’t see in this list?
ANSWER - ^ ; to raise a value to certain exponent, we have to use the pow() function in C, which means we must include the math.h library.

## Slide 19: Mixed Mode Arithmetic ( / )
 | Float | Integer
Float | Float | Float
Integer | Float | Integer
#include <math.h>
…
float a=5,b=2, c, d, e;
int j=5, k=2, l=3.5;
c = a/b;
d = j/k;
e = j/b;
…
c = ?
d = ?
e = ?
l = ?
Notes: Instructor:
This is an incredibly important concept.
WHITEBOARD ACTIVITY – Have students determine the answers for c, d, e, and l.
The next slide contains the answer.

## Slide 20: Mixed Mode Arithmetic ( / )
 | Float | Integer
Float | Float | Float
Integer | Float | Integer
#include <math.h>
…
float a=5,b=2, c, d, e;
int j=5, k=2, l=3.5;
c = a/b;
d = j/k;
e = j/b;
…
c = 2.500000
d = 2.000000
e = 2.500000
l = 3
Notes: Instructor:
Since this is an incredibly important concept, make sure to go over the answers and why they appear the way they do.

## Slide 21: Assignment Operators
Assignment
= +=
-= /=
*= %=
…
int a = 10;
a += 2; // a = a + 2;
a -= 4; // a = a - 4;
a /= 4; // a = a / 4;
a *= 5; // a = a * 5;
a %= 4; // a = a % 4;
…
a = 10
a = 12
a = 8
a = 2
a = 10
a = 2
Notes: Instructor:
Make sure to point out to the students the commented portion is the long version of the assignment operator.
This is another opportunity to make a comparison to MATLAB. In MATLAB, we were not able to use the “short” version of the assignment operators.

## Slide 22: Increment/Decrement Operators
Before line executes
++var
--var
After line executes
var++
var--
…
int a = 9, b = 4, c = 0;
fprintf(stdout,"%i %i %i\n",a,b,c);
c = a++;
fprintf(stdout,"%i %i %i\n",a,b,c);
c = --b;
fprintf(stdout,"%i %i %i\n",a,b,c);
…
Notes: Instructor:
This is something else that wasn’t available in MATLAB.
WHITEBOARD ACTIVITY – Have students determine the output.
The next slide contains the answer.

## Slide 23: Increment/Decrement Operators
Before line executes
++var
--var
After line executes
var++
var--
9 4 0
10 4 9
10 3 3
…
int a = 9, b = 4, c = 0;
fprintf(stdout,"%i %i %i\n",a,b,c);
c = a++;
fprintf(stdout,"%i %i %i\n",a,b,c);
c = --b;
fprintf(stdout,"%i %i %i\n",a,b,c);
…
Notes: Instructor:
Spend some time making sure students understand why the output looks the way it does.

## Slide 24: Relational & Logical Operators
Relational
< <= ==
> >= !=
Logical
! && ||
…
int a=1,b=0,c=-1;
int d,e,f,g,h,i;
d = a<b;
e = a==b;
f = a!=b;
g = b&&c;
h = b||c;
i = !c;
…
d = 0
e = 0
f = 1
g = 0
h = 1
i = 0
Notes: Instructor:
Opportunity to ask students what’s different about the relational and logical operators they used in MATLAB and the ones now available in C.

## Slide 25: Skeleton Program
/**************************************/
/* Name: Brutus Buckeye */
/* Seat No. 0, Instr: W. Hayes */
/* Program progname */
/**************************************/
#include <stdio.h>
#include <stdlib.h>
#include <math.h>
int main ( )
{
fprintf(stdout,"**************************************\n");
fprintf(stdout,"* Name: Brutus Buckeye *\n");
fprintf(stdout,"* Seat No. 0, Instr: W. Hayes *\n");
fprintf(stdout,"* Program progname *\n");
fprintf(stdout,"**************************************\n");
put code here ;
}
Notes: Instructor:
Point out to students that this is the structure we want them to use for their programs. It can save time in the future if students create a skeleton file like this containing their information that they can then copy for every assignment as opposed to rewriting this each time.

## Slide 26: Summary
C basics
Program structure
Data types
Operators
Questions?
Notes: Instructor:
The main objective of this class was to introduce students to C programming. After this lecture students should have a good understanding of the following:
C basics – including primary differences between MATLAB and C
The general structure students will use to write C programs
The declaration of variables and the common data types associated with variables students will use
Operators – including assignment, increment/decrement, relational, and logical. Students should recognize the similarities and differences between the operators in C and in MATLAB
The benefits of creating a skeleton program to use for their assignments
What questions are there?